## Slide 1: Creating AFGROW Plug-Ins for Stress Intensity Solutions
J.A. Harter, AFRL/VASM
Kyle Honeycutt, AP/ES, Inc.

## Slide 2
Joint Effort between AFRL, APES, Boeing, and LexTech, Inc.
Allows Users to Create/Animate Structural Models for Use in AFGROW
External DLL Code provides
  K solutions
  Crack Limits
  Drawing Functionality
  Parameters
  Parameter Default Values
  Error Checking
  Control of External K-Solver, if applicable
Background Information

## Slide 3: Requirements
Software with the ability to create ActiveX DLL files
  Microsoft Visual Basic (not VBA)
  Microsoft Visual C++
AFGROW Config File (afgrow.exe.config)
Tells AFGROW which Plug-Ins are available
Static Bitmap picture identifying Plug-In Geometry and Parameters
A DLL File meeting AFGROW functional requirements
Required Functions, subroutines, properties, and events

## Slide 4: What is a DLL?
A DLL (Dynamic Link Library) contains executable functions or data needed to run the application with which it is associated
The DLL server waits for a client (the AFGROW executable) to query it or pass it information.
AFGROW requires the Plug-In DLL to provide certain pieces of data and provide certain functions that will respond to AFGROW requests

## Slide 5: Creating Plug-In Modules Using Visual BASIC

## Slide 6: Create a Class
A class is a blueprint or prototype that defines the variables and the methods common to all objects of a certain kind

## Slide 7: AFGROW Reference
Add Visual Basic Reference to AFGROW so we can use the AFGROW COM objects
Create Instances of the AFGROW Drawing Window, the Prediction Manager, and invoke the Plug-In Functionality
( 1 )
( 2 )

## Slide 8: Required Objects
Private Property Get AfgrowBetaPlugin_bSolverVisible() As Boolean: End Property Private Property Let AfgrowBetaPlugin_bSolverVisible(ByVal Value As Boolean): End Property Private Function AfgrowBetaPlugin_GetVersion() As String: End Function Private Function AfgrowBetaPlugin_GetName() As String: End Function Private Function AfgrowBetaPlugin_GetDescription() As String: End Function Private Function AfgrowBetaPlugin_GetSolverVersion() As String: End Function Private Function AfgrowBetaPlugin_GetParameterList() As Variant: End Function Private Function AfgrowBetaPlugin_CountParameters() As Long: End Function Private Function AfgrowBetaPlugin_GetDoubleParameterValue(ByVal sID As String) As Double: End Function Private Function AfgrowBetaPlugin_GetDoubleParameterDefaultValue(ByVal sID As String) As Double: End Function Private Function AfgrowBetaPlugin_GetParameterName(ByVal sID As String) As String: End Function Private Function AfgrowBetaPlugin_GetParameterDescription(ByVal sID As String) As String: End Function Private Function AfgrowBetaPlugin_SetDoubleParameterValue(ByVal sID As String, ByVal dValue As Double) As String: End Function Private Function AfgrowBetaPlugin_GetModelPicture() As stdole.Picture: End Function Private Sub AfgrowBetaPlugin_SetSpecimenDrawInt(ByVal IDraw As Afgrow.IAfgrowSpecimenDrawInt): End Sub Private Sub AfgrowBetaPlugin_SetPredictManageInt(ByVal IManage As Afgrow.IAfgrowPredictManageInt): End Sub Private Sub AfgrowBetaPlugin_PredictEvent(ByVal iAfgrowEventID As Afgrow.AfgrowNotificationEvent): End Sub Private Function AfgrowBetaPlugin_GetEnumParameterValue(ByVal sID As String) As Long: End Function Private Function AfgrowBetaPlugin_GetEnumParameterDefaultValue(ByVal sID As String) As Long: End Function Private Function AfgrowBetaPlugin_SetEnumParameterValue(ByVal sID As String, ByVal iValue As Long) As String: End Function Private Function AfgrowBetaPlugin_GetParameterType(ByVal sID As String) As Afgrow.AfgrowPluginParameterType: End Function Private Function AfgrowBetaPlugin_GetEnumParameterList(ByVal sID As String) As Variant: End Function Private Function AfgrowBetaPlugin_GetStatusBarEventText(ByVal iAfgrowEventID As Afgrow.AfgrowNotificationEvent) As String: End Function

## Slide 9: Plug-In Bitmap w/Parameters
Add a picture for the model
  Recommended specs:
  GIF or BMP
  285 pixels wide
  341 pixels high
  Background RGB = 212,208,200
Set up local variables for our plug-in class, independent of AFGROW, for error checking purposes
  “d” is the recommended coding convention for a double-precision variable: dC, dL1, dL2, dR1, ….

## Slide 10: Define the Model
Private Sub Class_Initialize()
'Initialize Local Variables
dC = 0.2
dL1 = 0.6
dL2 = 0.5
dR1 = 1#
dR2 = 0.7
dt = 0.25
dCinitial = 0.2
End Sub
Private Function AfgrowBetaPlugin_GetDescription() As String
' Provides description of the Plug-In in the Plug-In Dialog
AfgrowBetaPlugin_GetDescription = "S-Section Example"
End Function
Private Function AfgrowBetaPlugin_GetModelPicture() As stdole.Picture
'Displays the picture of the model in the Plug-In dialog box
Dim Picture As IPictureDisp
Set Picture = LoadPicture(App.Path & "\SSection.bmp")
Set AfgrowBetaPlugin_GetModelPicture = Picture
End Function
Private Function AfgrowBetaPlugin_GetName() As String
' Displays model name in drawing window and parameter list
AfgrowBetaPlugin_GetName = "Thru-Crack in an S-Section"
End Function

## Slide 11: Establish Parameters
Private Function AfgrowBetaPlugin_CountParameters() As Long
'Number of parameters
AfgrowBetaPlugin_CountParameters = 6
End Function
Private Function AfgrowBetaPlugin_GetParameterList() As Variant
' Establish the list of parameters for AFGROW
Dim aParam(5) As String
aParam(0) = "C"
aParam(1) = "L1"
aParam(2) = "L2"
aParam(3) = "R1"
aParam(4) = "R2"
aParam(5) = "t"
AfgrowBetaPlugin_GetParameterList = CVar(aParam)
End Function

## Slide 12: Establish Parameters
Private Function AfgrowBetaPlugin_GetParameterName(ByVal sID As String) As String
' Provides a description of each parameter
Select Case sID
Case "C": AfgrowBetaPlugin_GetParameterName = "Crack Length"
Case "L1": AfgrowBetaPlugin_GetParameterName = "Bottom Length"
Case "L2": AfgrowBetaPlugin_GetParameterName = "Top Length"
Case "R1": AfgrowBetaPlugin_GetParameterName = "Bottom Radius"
Case "R2": AfgrowBetaPlugin_GetParameterName = "Top Radius"
Case "t": AfgrowBetaPlugin_GetParameterName = "Thickness"
End Select
End Function
Private Function AfgrowBetaPlugin_GetDoubleParameterValue(ByVal sID As String) As Double
' AFGROW gets the parameter values
Select Case sID
Case "C": AfgrowBetaPlugin_GetDoubleParameterValue = dC
Case "L1": AfgrowBetaPlugin_GetDoubleParameterValue = dL1
Case "L2": AfgrowBetaPlugin_GetDoubleParameterValue = dL2
Case "R1": AfgrowBetaPlugin_GetDoubleParameterValue = dR1
Case "R2": AfgrowBetaPlugin_GetDoubleParameterValue = dR2
Case "t": AfgrowBetaPlugin_GetDoubleParameterValue = dt
End Select
End Function

## Slide 13: Set Parameters
Private Function AfgrowBetaPlugin_SetDoubleParameterValue(ByVal sID As String, ByVal dValue As Double) As String
' AFGROW sets (returns) the parameter values to the Plug-In module
Dim vOldValue As Variant
Select Case sID
Case "C": vOldValue = dC: dC = dValue
Case "L1": vOldValue = dL1: dL1 = dValue
Case "L2": vOldValue = dL2: dL2 = dValue
Case "R1": vOldValue = dR1: dR1 = dValue
Case "R2": vOldValue = dR2: dR2 = dValue
Case "t": vOldValue = dt: dt = dValue
End Select
If ErrorCheck = "" Then
Annimate
Else
AfgrowBetaPlugin_SetDoubleParameterValue = ErrorCheck
Select Case sID
Case "C": dC = vOldValue
Case "L1": dL1 = vOldValue
Case "L2": dL2 = vOldValue
Case "R1": dR1 = vOldValue
Case "R2": dR2 = vOldValue
Case "t": dt = vOldValue
End Select
End If
End Function

## Slide 14: Error Checking
Private Function ErrorCheck() As String
'Checks for error(s) in parameter values, returns a null string if no errors are found
dMaxC = dL1 + dL2 + 4 * Atn(1) * (dR1 + dR2 + dt)
ErrorCheck = ""
If dC < 0.005 Then ErrorCheck = ErrorCheck & "C must be > 0.005" & Chr(13) & Chr(10)
If dC >= dMaxC Then ErrorCheck = ErrorCheck & "C must be <= " & dMaxC & Chr(13) & Chr(10)
End Function

## Slide 15: Drawing to the Animation Frame
AFGROW automatically scales and adds a border to your drawing
Origin is at top left, positive Y is downward
Some Available Drawing Functions:
  AddPoligon(aX, aY, iBgColor As AfgrowBackgroundColorSpecimenDrawing)
  AddRectangle(left As Double, top As Double, right As Double, bottom As Double, iBgColor As AfgrowBackgroundColorSpecimenDrawing)
  AddPath(sID As String, iBgColor As AfgrowBackgroundColorSpecimenDrawing)
  AddLinesToPath(sPathID As String, aX, aY)
  AddArcToPath(sPathID As String, left As Double, top As Double, right As Double, bottom As Double, startAngle As Double, sweepAngle As Double)

## Slide 16: Drawing Tools
Private Function Animate()
ISpecimenDraw.Reset
Dim x(2) As Double, y(2) As Double
x(0) = 0: y(0) = 0
x(1) = 0.15: y(1) = 1
x(2) = 1: y(2) = 0.5
ISpecimenDraw.AddPath "path1", BackgroundSpecimen
ISpecimenDraw.AddLinesToPath "path1", x, y
End Function
Private Function Animate()
ISpecimenDraw.Reset
Dim x(2) As Double, y(2) As Double
x(0) = 0: y(0) = 0
x(1) = 0.15: y(1) = 1
x(2) = 1: y(2) = 0.5
ISpecimenDraw.AddPath "path1", BackgroundSpecimen
ISpecimenDraw.AddLinesToPath "path1", x, y
ISpecimenDraw.AddArcToPath "path1", 0.5, -0.5, 1.5, 0.1, 90, 110
End Function

## Slide 17: Draw to the Animation Frame
Private Function Animate()
Dim x(3) As Double, y(3) As Double
Dim dLength As Double
Dim dSweep1, dSweep2 As Double
'Draw specimen and animate crack growth
DrawTool.Reset
'Draw Specimen
DrawTool.AddPath "Path1", BackgroundSpecimen
DrawTool.AddArcToPath "Path1", dL1 - dR2 - dt, 0, dL1 + dR2 + dt, 2 * dt + 2 * dR2, 90, 180
DrawTool.AddLineToPath "Path1", dL1 + dL2, 0, dL1 + dL2, dt
DrawTool.AddArcToPath "Path1", dL1 - dR2, dt, dL1 + dR2, dt + 2 * dR2, -90, -180
DrawTool.AddArcToPath "Path1", dL1 - dR1 - dt, dt + 2 * dR2, dL1 + dR1 + dt, 3 * dt + 2 * dR1 + 2 * dR2, -90, 180
DrawTool.AddLineToPath "Path1", 0, 3 * dt + 2 * dR1 + 2 * dR2, 0, 2 * dt + 2 * dR1 + 2 * dR2
DrawTool.AddArcToPath "Path1", dL1 - dR1, 2 * dt + 2 * dR2, dL1 + dR1, 2 * dt + 2 * dR1 + 2 * dR2, 90, -180
'Draw Crack
dLength = dC
If dLength > dL1 Then dLength = dL1
DrawTool.AddPath "Path2", BackgroundCrack
x(0) = dLength: y(0) = 3 * dt + 2 * dR1 + 2 * dR2
x(1) = 0: y(1) = 3 * dt + 2 * dR1 + 2 * dR2
x(2) = 0: y(2) = 2 * dt + 2 * dR1 + 2 * dR2
x(3) = dLength: y(3) = 2 * dt + 2 * dR1 + 2 * dR2

## Slide 18: Draw to the Animation Frame
DrawTool.AddLinesToPath "Path2", x, y
If dC > dL1 Then
dSweep1 = (dC - dL1) * 180 / 4 * Atn(1) / (dR1 + dt / 2)
If dSweep1 > 180 Then
dSweep1 = 180
dSweep2 = (dC - dL1 - 4 * Atn(1) * (dR1 + dt / 2)) * 180 / 4 * Atn(1) / (dR2 + dt / 2)
End If
DrawTool.AddArcToPath "Path2", dL1 - dR1, 2 * dt + 2 * dR2, dL1 + dR1, 2 * dt + 2 * dR1 + 2 * dR2, 90, -dSweep1
If dSweep1 = 180 Then
If dSweep2 > 180 Then dSweep2 = 180
DrawTool.AddArcToPath "Path2", dL1 - dR2 - dt, 0, dL1 + dR2 + dt, 2 * dt + 2 * dR2, 90, dSweep2
If dSweep2 = 180 Then
dLength = dC - 4 * Atn(1) * (dR1 + dR2 + dt)
x(0) = dL1: y(0) = 0
x(1) = dLength: y(1) = 0
x(2) = dLength: y(2) = dt
x(3) = dL1: y(3) = dt
DrawTool.AddLinesToPath "Path2", x, y
End If
DrawTool.AddArcToPath "Path2", dL1 - dR2, dt, dL1 + dR2, dt + 2 * dR2, 90 + dSweep2, -dSweep2
End If
DrawTool.AddArcToPath "Path2", dL1 - dR1 - dt, dt + 2 * dR2, dL1 + dR1 + dt, 3 * dt + 2 * dR1 + 2 * dR2, 90 - dSweep1, dSweep1
End If
End Function

## Slide 19: Manage Prediction
Private Sub AfgrowBetaPlugin_SetPredictManageInt(ByVal IManage As Afgrow.IAfgrowPredictManageInt)
Set PredictManage = IManage
End Sub
Private Sub AfgrowBetaPlugin_PredictEvent(ByVal iAfgrowEventID As Afgrow.AfgrowNotificationEvent)
Select Case iAfgrowEventID
Case AfgrowNotificationEvent.AfgrowEventPredictStarted: Call CreateCrack
Case AfgrowNotificationEvent.AfgrowEventCalculateBeta: Call CalculateBeta
Case AfgrowNotificationEvent.AfgrowEventOutput
dC = PredictManage.GetCrackDirectionParameter("Crack One", "C", "length")
Annimate
Case AfgrowNotificationEvent.AfgrowEventCrackFailure: Call ResetStartingCrackLength
Case AfgrowNotificationEvent.AfgrowEventCrackTransition:
Case AfgrowNotificationEvent.AfgrowEventError:
Case AfgrowNotificationEvent.AfgrowEventPredictFinished: Call ResetStartingCrackLength
End Select
End Sub

## Slide 20: Manage Prediction
Private Sub CreateCrack()
PredictManage.AddCrack "Crack One"
PredictManage.AddCrackDirection "Crack One", "C"
PredictManage.SetCrackDirectionParameter "Crack One", "C", "length", dC
PredictManage.SetCrackDirectionParameter "Crack One", "C", "length_initial", dC
PredictManage.SetCrackDirectionParameter "Crack One", "C", "length_limit", dMaxC
dCinitial = dC
End Sub
Private Sub CalculateBeta()
Dim Beta As Double
Dim RootPiC As Double
dC = PredictManage.GetCrackDirectionParameter("Crack One", "C", "length")
RootPiC = PredictManage.GetCrackDirectionParameter("Crack One", "C", "sqrt_pi_length")
Beta = 1.12 * Sqr(1 / Cos(4 * Atn(1) / 2 * dC / dMaxC))
PredictManage.SetCrackDirectionParameter "Crack One", "C", "alfa", Beta * RootPiC
End Sub
Private Sub ResetStartingCrackLength()
' Reset crack length to the initial value
dC = dCinitial
End Sub

## Slide 21: Add DLL to the AFGROW Directory
Compile the DLL
Copy the DLL and Model Bitmap (or GIF) to the AFGROW Director
Register the DLL
Modify the afgrow.exe.config file:
<?xml version="1.0" encoding="utf-8" ?>
<configuration>
<appSettings>
<add key="Application Name" value="MyApplication" />
</appSettings>
<custom.settings>
<plugins>
<plugin>Project1.Class1</plugin>
</plugins>
</custom.settings>
</configuration>
Project Name
Class Name

## Slide 22: Select New Plug-In Model

## Slide 24: Summary
Plug-Ins allow User-Defined Custom Solutions
  Proprietary
  Closed-Form
  Tabular / Interpolative / Extrapolative
  External-K
AFGROW can theoretically handle an unlimited # of crack parameters, unlimited # of cracks
If the getBeta function is time-consuming, do not set AFGROW’s “Max Growth Increment” value too small! Do not run cycle-by-cycle beta calculation!